North Tyneside Council
Hackney Carriage and Private Hire Licensing Policy

Vehicle Testing Arrangements – Components to be Inspected

Body / Vehicle Structure / Free from excessive corrosion or damage in specific areas. No sharp edges likely to cause injury.
Speedometer/Odometer / Condition and operation.
Fuel System / No leaks. Security and condition of pipes/hoses. Fuel cap fastens and seals securely.
Exhaust Emissions / Vehicle meets the requirements for exhaust emissions, dependent on the age and fuel type of the vehicle.
Exhaust System / Secure. Complete. Catalyst missing where one was fitted as standard. Without serious leaks and is not too noisy.
Seat Belts / All the seat belts fitted are checked for type, condition, operation and security. All mandatory seat belts must be in place. Check of the Malfunction Indicator Lamp (MIL) for air bags and seat belt pre tensioners and load limiters.
Seats / Driver’s seat for adjustment. All seats for security and seat backs can be secured in the upright position.
Doors / Latch securely in closed position. Front doors should open from the inside and outside the vehicle. Rear doors should open from outside the vehicle. Hinges and catches for security and condition.
Mirrors / Minimum number required, condition and security. Indirect vision devices.
Load Security / Boot or tailgate can be secured in the closed position.
Brakes / Condition including inappropriate repairs or modifications, operation and performance (efficiency test). Note the removal of the road wheels and trims are not part of the test. Anti-lock Braking System (ABS) and Electronic Stability Control (ESC) where fitted. Check of the dashboard Malfunction Indicator Lamp (MIL) for ABS, ESC, electronic park brake and brake fluid warning.
Tyres and Wheels (including spare) / Condition, security, tyre size/type and tread depth. Note: vehicles first used on or after 1st January 2012 – check of the MIL for Tyre Pressure Monitoring System (TPMS).
Registration Plates / Condition, security, colour, characters correctly formed and spaced.
Lights / Condition, operation including High Intensity Discharge (HID) and Light Emitting Diode (LED) headlamps for cleaning, self-levelling and security. Headlamp aim. Main beam warning light.
Bonnet / Securely latches in the closed position.
Wipers / Washers / Operate to give the driver a clear view ahead.
Windscreen / Condition and driver’s view of the road.
Horn / Correct operation and of suitable type.
Steering and Suspension / Condition, steering oil level, operation, a check for inappropriate repairs or modification including corrosion to power steering pipes or hoses. Operation of steering lock mechanism. Check of MIL for electronic power steering and steering lock.
Towbars (if fitted) / Security/condition/inappropriate repairs or modification. Correct operation of 13 pin electrical socket.
Vehicle Identification Number / Present on vehicles first used on or after 1st August 1980. A single VIN is displayed except on multistage build vehicles (e.g. van conversion, BMW/ Alpina).
Electrical / Visible electrical wiring and battery
Vehicle Interior / Clean.
Vehicle Exterior / Uniform colour.
Glass / Windscreen - minimum 75% light transmittance. / Front side windows - minimum 70% light transmittance / If tinted windows are fitted as standard there will be no minimum light transmission to the rear of the B pillar. / All other windows – minimum 34% light transmittance
Meter (if fitted) / Must be of an approved type and sealed.
Spare Wheel / The vehicle shall be equipped with either: / A spare wheel of full or space save design above the legal tread requirement and the tools to change a wheel, or / An emergency puncture repair kit (to include compressor/inflator) or / Run flat tyres or / Provide evidence of a contract with a mobile tyre replacement specialist.
Wheel-brace & Jack (only if spare wheel present) / Present. Correct operation.
Luggage Accommodation / Compartment clean, empty.
Seats & Interior Trim / Clean, free from rips or tears.
Floor Covering / Clean. No obstructions.
Licence Plate (Annual and Interim Tests Only) / Present. Securely attached to vehicle. Correct location on vehicle. In satisfactory condition and information legible
NTC Windscreen Disc / Present. Securely attached to windscreen. In satisfactory condition, information legible.
NTC Door Signs / Present. Fitted correctly. In satisfactory condition, information legible.
NTC Emergency/ Information Signs (Minibuses/PCV’s) / Present. In satisfactory condition, information legible.
For Hire Sign (hackney carriage only) / Present. Works in conjunction with meter and roof-sign.
Roof Sign (Hackney carriages only) / Present. Correct type and size for type of vehicle. Correct colours. Lettering correct size.
Advertising - bodywork / Approved. Present only on rear doors & boot area of vehicle unless approved.
Advertising - glass / Approved. Present only on top edge of windscreen.
NTC Fare Table (hackney carriage only) (Dashboard/partition/Rear Windows) / Present. In satisfactory condition. Most recent issue.
Byelaws (hackney carriage only) / Present. Satisfactory condition and legible
Interior Door Locks (Purpose built hackney carriage only) / Work in conjunction with foot-brake.
Ramps (if present) / Present. Stored securely. Adequate locking device must be fitted to ensure the ramps do not slip or tilt when in use.
Wheelchair Anchorages (if applicable) / Must be of an approved type (chassis or floor linked and capable of withstanding approved dynamic or static tests).
Tail-Lifts (if present) / Must have valid LOLER Certificate. Tail lift must not prevent the rear door(s) from being opened and must be easily moved if the power supply fails.
Wheelchair Anchorages (if applicable) / Must be of an approved type (chassis or floor linked and capable of withstanding approved dynamic or static tests).
Tail-Lifts (if present) / Must have valid LOLER Certificate. Tail lift must not prevent the rear door(s) from being opened and must be easily moved if the power supply fails.